## Slide 1: Error Detection & Correction Control
In data communication, Error may occur due to signal attenuation, natural phenomenon such as lightning, which will affect a set of bits for a short time.
Detecting and correcting errors requires redundancy - sending additional information along with the data.
Error Detection
Error detection is performed by calculating an error-detection code that is a function of bits being transmitted. The code is appended to the transmitted bits. The receiver calculates the code based on the incoming bits and compare it to the incoming code to check for errors.
Error Correction
operates in a fashion similar to error detection but is capable of correcting certain errors in a transmitted bit stream.

## Slide 2
Types of Errors
single bit error, burst error
There are two type of errors may occur during the transmission. Single bit error and burst error.
Single Bit Error: Only one bit in the data unit has changed.
Burst Error: Two or more bits in the data unit have changed. The length of the burst is measured from the first corrupted bit to the last corrupted bit.
0
1
0
1
0
1
0
0
1
0
0
0
1
0
0
1
0
0
1
1
0
0
1
1
1
0
1
0
Sent
received
Length of burst error (8 bits)
Bits corrupted

## Slide 3: Redundancy
There are two ways of handling transmission errors:
Error Detection and correction: Include enough redundancy to detect and correct errors.
Error Detection and retransmission:. Include enough redundancy bits to detect errors and use ACKs and retransmissions to recover from the errors.
redundancy means adding extra bits to data unit for detecting errors at the receiver.

## Slide 4: Error Detection
Vertical Redundancy Check: (Parity Check):
A parity bit is added to every data unit so that the total number of 1s becomes even.
Detection Methods
VRC
LRC
CRC
Checksum
VRC can detect all single bit errors. It can detect burst errors only if the total number of errors in each data unit is odd.
1100001
Even
parity
generator
11000011
Checking
function
receiver
sender
VRC (parity bit)
data

## Slide 5: Longitudinal Redundancy Check (LRC)
A block of bits is arranged in the matrix form and redundancy check (parity) is computed column wise. A redundant row of bits is added to the whole block.
Data: 11100111 11011101 00111001 10101001
0
1
0
1
0
1
0
1
1111
1000
1100
0111
0110
1011
1100
1101
LRC
VRC (parity row)
Data + LRC 11100111 11011101 00111001 10101001 10101010
Direction of movement
A LRC of n bits can easily detect a burst error of n bits.

## Slide 6: Cyclic Redundancy Check (CRC): Modulo 2 Arithmetic
Given a k-bit block of bits or message, the sender generate an n – k bit sequence, known as a CRC, such that the resulting frame consisting of n bits, is exactly divisible by some predetermined number (divisor) of length n - k +1. The receiver then divides the incoming frame by that number and , if there is no remainder, assumes there is no error.
Data
00..0
Divisor
CRC
k
n - k
(n – k + 1)
Remainder
(n – k)
Data
CRC
Divisor
Remainder
Data
CRC
Receiver
Sender
zero – no error
nonzero - error
T = n-bit frame to be transmitted
D = k-bit block of data or message
R = (n - k) bits CRC
P = pattern of n – k +1 bits; that is the predetermined divisor. The pattern p is chosen to be one bit longer than the CRC. The higher and lower order bits of P must be 1
Mathematically, It can describes as using modulo 2 arithmetic:

## Slide 7
The errors in an n-bit frame can be presented by an n-bit filled with 1s in each error position.
T = Transmitted frame
E = Error pattern with 1s in positions where errors occur.
Tr = Received frame
If there is an error ( E ≠ 0), the receiver will fail to detect the error if and only if Tr is divisible by P, which is equivalent to E divisible by P
Modulo 2 Arithmetic:
Module 2 arithmetic uses binary addition with no carries (XOR), and binary subtraction with no carries also interpreted as the (XOR) operation.
1111 1111
+1010 -0101
0101 1010

## Slide 8: Example of CRC using Modulo 2 Arithmetic
Message D = 1010001101
Pattern P = 110101
CRC R = to be calculated
Thus n = 15, k = 10, and (n – k) = 5
The message is multiply by 25 :
25 D = 101000110100000
This product is divided by P,
gives the remainder R = 01110
The remainder is added to 25D ( T = 25D + R) to give
T = 1010001101 01110 , which is transmitted.
CRC
Sender

## Slide 9: At the receiver
If receiver receives the frame T, which is divided by P
remainder
There is no remainder, it is assumed that there is no errors.

## Slide 10: Example In a CRC detection scheme, choose P = 10011, message M = 10010011011. find the CRC and frame T. a. Suppose the channel introduces an error pattern 100010000000000. (a flip from 1 to 0 or 0 to 1in position 1 and 5). What is received. Can the error be detected? b. Repeat the part a with error pattern 100110000000000.
Sol.
After calculation, CRC bits are 1100. The frame T= 100100110111100 is sent.
a. Tr = E  T
Tr = 100010000000000 
100100110111100
Frame 000110110111100 is received. Tr is divided by P,
The remainder after division by P is 1110 ,which is nonzero. The errors are detected.
b. Tr = E  T
Tr = 100110000000000  100100110111100
The string 000010110111100 is received, The remainder after division by P is zero. The errors are not detected

## Slide 11: Cyclic Redundancy Check (CRC): Polynomial Method All values of CRC process can be express as polynomials in a dummy variable X, with binary coefficients. Thus for ,
Arithmetic operations are modulo 2. The CRC process can now be described as:
n- no of bits in a frame to be transmitted
k- no of bits block of data or message
(n - k) bits CRC
(n-k+1) bits divisor (generator polynomial)

## Slide 12
Example of CRC using polynomial division:
R(X)

## Slide 13
Checksum
This error detection method is used by higher layer protocol (Transport Layer).
The sender follows these step:
The data unit is divided into k sections, each of n bits.
All sections are added together using one’s complement to the sum.
The sum is complemented and become the checksum.
The checksum is sent with the data.
The receiver follows these step:
The data unit is divided into k sections, each of n bits.
All sections are added together using one’s complement to the sum.
The sum is complemented.
If the result is zero, the data are accepted: otherwise, they are rejected.

## Slide 14
Example of checksum
Suppose the following block of 24 bits is to be sent using a checksum of 8 bits.
10101011 00101101 10010101, what is the resulting frame to be transmitted?
The data unit is divided into 3 section of each 8 bits. And added using one’s complement arithmetic.
Sender
Receiver
Receiver receives the frame:
10101011 00101101 10010101 10010001
The pattern is divided into 4 section of each 8 bits and added using one’s complement arithmetic.

## Slide 15: Error Correction Codes
Relationship between data bits and redundancy bits to correct single bit error:
A frame consists of m data bits and r redundant or check bits. Let the total length of frame be n ( i.e. n = m + r). A n-bit unit containing data and check bit is often referred to as an n-bit codeword.
Number of states of single bit error = m + r
Number of state for no error = 1
So, number of redundant bit (r) that represent all states m+r+1 must satisfy
m | r

## Slide 16
Hamming code
This method uses extra parity bits to allow the identification of a single bit error. Create the codeword as follows:
Mark all bit positions that are powers of two as parity bits (1, 2, 4, 8, 16, 32, 64, 128, etc).
All other bit positions are for the data to be encoded (3, 5, 6, 7, 9, 10, 11, etc).
Each parity bit calculates the parity for some of the bits in the codeword. The position of the parity bit determines the sequence of bits that it alternately checks and skips.
Position 1: ckeck1 bit, skip 1 bit, check 1 bit, skip 1 bit, ...
(1, 3, 5, 7, 9, 11, …)
Position 2: check 2 bit, skip 2 bit, check 2 bit, skip 2 bit,…
(2, 3, 6, 7, 10, 11, 14, 15, …)
Position 4: check 4 bit, skip 4 bit, check 4 bit, skip 4 bit,…
(4,5,6,7, 12,13,14,15, 20,21,22,24, …)
position 8: check 8 bit, skip 8 bit, check 8 bit, skip 8 bit,…
(8,9,10,11,12,13,14,15, 24,25,26,27,28,29,30,31, …)
…………
Set the parity bit 1 if the total number of 1s in the potions it check is odd.
set the parity bit 0 if the total number of 1s in the potions it check is even.

## Slide 17
Example: Hamming codeword
To construct the even parity hamming codeword for a data byte : 10011010.
To create the codeword, leaving the spaces for the parity bits.
_ _ 1 _ 0 0 1 _ 1 0 1 0
Position 1: check data bits 1, 3, 5, 7, 9, 11.
? _ 1 _ 0 0 1 _ 1 0 1 0 even parity, set bit position 1 0.
0 _ 1 _ 0 0 1 _ 1 0 1 0
Position 2: check bit 2, 3, 6, 7, 10, 11.
0 ? 1 _ 0 0 1 _ 1 0 1 0 odd parity, set bit position 2 to 1.
0 1 1 _ 0 0 1 _ 1 0 1 0
Position 4: check bit, 4,5,6,7.
0 1 1 ? 0 0 1 _ 1 0 1 0 odd parity, set bit position 4 to 1.
0 1 1 1 0 0 1 _ 1 0 1 0
position 8: check bit 8,9,10,11,12
0 1 1 1 0 0 1 ? 1 0 1 0 even parity, set bit position 8 to 0
0 1 1 1 0 0 1 0 1 0 1 0
Codeword : 0 1 1 1 0 0 1 01 0 1 0

## Slide 18
Finding and Fixing a bad bit in Hamming codeword
Check each parity bit, and add the positions that are wrong, this will give you the location of the bad bit.
Example:
The last example created a codeword 011100101010.
Suppose the codeword was received as 011100101110.
Verify each check bits, you will discover that parity bits 2 and 8 are incorrect. so,
2 + 8 = 10.
10th position is the location of the bad bit. So correct codeword is : 011100101010
10101101110